## Slide 1: Effect of grid resolution on ocean simulations in the Labrador Sea using NEMO and AGRIF
Clark Pennelly
Xianmin Hu
Paul G. Myers
Department of Earth and Atmospheric Sciences
University of Alberta

## Slide 2: Outline
Nesting software: AGRIF
Modeling framework: NEMO
Simulation configurations
Comparison of simulations
Ongoing/future work

## Slide 3
AGRIF: Adaptive Grid Refinement In Fortran1
1Debreu, Laurent, Christophe Vouland, and Eric Blayo. "AGRIF: Adaptive grid refinement in Fortran." Computers & Geosciences 34.1 (2008): 8-13.
AGRIF
Transformation
(1:3 ratio)
Control
Grid Box
1/4°
1/12°
1/12°
1/4°
AGRIF Grid Boxes
X:814
Y:544
X:270
Y:180
Parent
1/4°
Example: Simulation using one nest
AGRIF
1/12°

## Slide 4: AGRIF features
Nest simulation runs alongside parent
Nest requires a complete separate set data
Computationally expensive
1-way or 2-way feedback between nest and parent
Parent time step:
Supply BC
AGRIF time step:
Interpolate to parent
1/12° IC & forcing data
dt=540s
dt=180s

## Slide 5: Why use nests?
Hallberg (Ocean Mod. 2013)
High resolution is needed to resolve eddies
More realistic simulation of small scale features: bathymetry, boundary currents, etc
Computationally cheaper than high resolution across entire domain

## Slide 6: NEMO
Numerical ocean modeling framework with multiple models available to use:
  Blue ocean: Ocean dynamics model
  White ocean: Sea ice model
  Green ocean: Biogeochemical model
  Mesh refinement software: AGRIF
  Tracer package
AGRIF
Future plans
Operational

## Slide 7: NEMO Simulation Settings
NEMO version 3.4
Ice Model: LIM2
50 vertical levels
Open Boundaries: Bering strait, 20°S
Initial Conditions: (3D) T, S, U, V, and (2D) SSH, Ice
Forcing: Hourly wind, rain, snow, LW/SW, air temp, air humidity from Environment Canada- GDPS
ANHA:
Arctic Northern Hemisphere Atlantic

## Slide 8: Simulations 2002-2010
Configuration | ANHA4 | ANHA12 | AGRIF12
Time step | 1080s | 180s | 540s : 180s
Horz. Resolution | 1/4° | 1/12° | 1/4° : 1/12°
Simulation time | ~4 days | 54+ days | ~28 days
CPUs used | 64 | 256 | 48
Core years | 0.7 | 37.8 | 3.7
Horizontal mesh
(km)
AGRIF12 (within ANHA4)
ANHA12
ANHA4
0
5
10
15
20
25
30

## Slide 9: Science questions
Resolution: does higher resolution resolve some important processes in Labrador Sea?
What is the fate of freshwater from off the West Greenland shelf?

## Slide 10: Eddy Kinetic Energy:sqrt [cm/s]
Same Forcing/IC
Same
Resolution
ANHA4
ANHA4-Runoff
AGRIF12
ANHA12

## Slide 11: Ongoing work: Double(+) Nesting
724
1204
604
769
544
800
0
5
10
15
20
25
30
1/36°
(1.4 to 2.0 km)
1/12°
1/4°

## Slide 12: Computation Cost of Simulations
Configuration | ANHA4 | ANHA12 | AGRIF12 | AGRIF 36 | ANHA36 (est)
Time step | 1080s | 180s | 540s : 180s | 540s: 180s: 60s | 60s
Horz. Resolution | 1/4° | 1/12° | 1/4° : 1/12° | 1/4° : 1/12° : 1/36° | 1/36°
Simulation time | ~4 days | 54+ days | ~28 days | ~2100 days (4 cpus) | ~1500 days
CPUs used | 64 | 256 | 48 | 4 | 256
Core years | 0.7 | 37.8 | 3.7 | 23 | ~1000
AGRIF provides a way to have high resolution numerical simulations with a dramatic reduction in computational cost